## Slide 1: Speculative Multithreaded Processors
Nicolae-Andrei Vasile

## Slide 2: OVERVIEW
speculation is a well-known technique used to improve processor performance
the task of dividing programs into threads that will be executed in parallel becomes hard for irregular and non-numerical programs
compilers usually fail to discover the potential thread-level parallelism that could be effectively exploited in this class of applications
speculative multithreading is a promising approach to solving the problem
performance of speculative multithreaded architectures is very sensitive to the policies that determine which parts of the code are executed by speculative threads and when they start execution

## Slide 3: SPECULATIVE THREAD-LEVEL PARALLELISM
thread spawning operation is identified by two instructions in the dynamic instruction stream (spawning and control quasi-independent points)
Thread Unit (TU) n executes the instruction stream in the same way as a conventional superscalar processor until it reaches a spawning point
the processor identifies a future instruction
Thread Unit (TU) n+1 spawns a new thread speculatively starting at the control quasi-independent point while Thread Unit n continues executing instructions

## Slide 4: SPECULATIVE MULTITHREADED PROCESSOR MICROARCHITECTURE
consists of several thread units (TU) that execute concurrently different threads of a sequential program
these threads are dynamically obtained by a control speculation mechanism
an important feature of SM processors is the aggressive use of speculation techniques
speculation mechanisms that can be classified into three categories:
  control speculation (used to obtain threads from a sequential program and to speculate on individual branches inside each thread like superscalar processors do)
  data dependence speculation (dependences among different threads - inter-thread dependences - are predicted by means of address prediction)
  data value speculation (inter-thread data dependences, either through registers or memory, do not cause a serialization between the producer)

## Slide 6: RELATED WORK
control speculation has been extensively researched
proposed schemes for superscalar processors are based on predicting branches in the sequential order of the program.
data dependence speculation is used by some processors in the memory disambiguation stage
few proposals in the literature dealing with the dynamic management of a large window that consist of several threads of control not necessarily independent among them obtained from a sequential program:
  SPSM architecture
  Superthreaded architecture
  Multithreaded Decoupled architecture
  etc.

## Slide 7: CONCLUSION
Speculative Multithreaded Processors (SMP) and related designs
ability to dynamically extract and execute multiple threads of control from a single sequential program written in a conventional ISA without requiring any compiler support
additional instruction level parallelism due to inter-thread parallelism hardly increases the fetch bandwidth requirements since multiple threads share the same code

## Slide 8: THANK YOU
Q&A